## Slide 1
MORSE CODE
Communication & Emergency Signaling System
An 8086 Assembly + Desktop-GUI Implementation
Mustafa Shahid
BSCS-14B | CMS ID: 500889
CS-234 Computer Organization & Assembly Language
Faculty: Dr. Omar Zeb · Sir Ijaz Alam Khan

## Slide 2
Presentation Outline
A roadmap for the next 13–16 minutes
BSCS-14B | 500889
▪ Why Morse? — motivation and real-world impact
▪ Problem statement and project objectives
▪ Literature review and background
▪ System architecture and block diagram
▪ Data structures and addressing modes
▪ Assembly walk-through (8086)
▪ Software interrupts and the IVT
▪ Desktop application — fourteen interactive pages
▪ Telegraph Key, Trainer and Cheat Sheet
▪ CPU simulator — registers, memory, flags, auto-play
▪ Live demonstration
▪ COAL concepts demonstrated
▪ Opportunities, challenges and ethics
▪ Conclusion and Q&A
Mustafa Shahid · CS-234 COAL Project
2 / 18

## Slide 3
Why Morse Code?
A 180-year-old idea that still saves lives
BSCS-14B | 500889
Real-world impact
Aviation beacons (VOR/NDB IDs), maritime distress, military field-comms, amateur radio, disaster response and accessibility for speech-impaired users.
Why it still wins
Needs only on/off signalling, survives extreme noise, works with milliwatts of power and is legible by the human ear alone.
Why it is perfect for COAL
Fixed-size lookup table ⇒ indexed addressing; I/O via INT 21h; tight loops, arithmetic and logical tricks such as AND AL, 0DFh for case conversion.
What this project delivers
Full 8086 program, modern Windows desktop GUI with audible beeps, live visualiser, emergency SOS and an in-app COAL concepts reference.
Mustafa Shahid · CS-234 COAL Project
3 / 18

## Slide 4
Problem Statement & Objectives
BSCS-14B | 500889
Problem
Build a compact COAL artefact that translates plain text into international Morse code, transmits it audibly and transparently demonstrates the major assembly-language concepts of the CS-234 syllabus.
Objectives
▪ Implement ASCII → Morse in 8086 assembly using a lookup table.
▪ Demonstrate direct, indirect, indexed and base+offset addressing.
▪ Use BIOS/DOS software interrupts for all I/O.
▪ Build a polished Windows GUI that mirrors the assembly behaviour.
▪ Include an emergency SOS broadcaster and a live visualiser.
▪ Deliver IEEE report, slides, viva guide and a runnable demo.
Mustafa Shahid · CS-234 COAL Project
4 / 18

## Slide 5
Literature & Background
BSCS-14B | 500889
ITU-R M.1677-1
The international standard for Morse timing: unit, dot, dash and inter-element gaps in ratios 1 : 1 : 3 : 1 : 3 : 7.
Hennessy & Patterson
Lookup tables are a canonical way to exploit locality of reference and map onto cache-friendly memory regions.
Irvine (x86 Assembly)
Reference text on addressing modes, interrupt usage and MASM programming style, followed closely in our code.
Intel 8086 Manual
Authoritative description of the ISA, the interrupt vector table and the DOS/BIOS service numbers used here.
Mustafa Shahid · CS-234 COAL Project
5 / 18

## Slide 6
System Architecture
Four layers, shared memory
BSCS-14B | 500889
+---------------------+ +----------------------+ | User Interface | <---> | Translation Engine | | (INT 21h / GUI) | | (ASCII -> Morse) | +---------------------+ +----------------------+ | | v v +---------------------+ +----------------------+ | Input/Output Buffer| | Morse Lookup Table | | (DS:input_buffer) | | (6-byte records) | +---------------------+ +----------------------+ | v +----------------------+ | Signal Generator | | (Beep / INT 21h/02) | +----------------------+
Mustafa Shahid · CS-234 COAL Project
6 / 18

## Slide 7
Lookup Table Layout
Six bytes per record → O(1) indexed access
BSCS-14B | 500889
Record: [ . . . . . ] [len]
byte 0-4 : Morse symbols (dots & dashes, space-padded) byte 5 : code length (1 – 5)
addr = morse_table + (index × 6)
▪ Letters 'A' .. 'Z' → index 0 .. 25
▪ Digits '0' .. '9' → index 26 .. 35
▪ Case conversion: AND AL, 0DFh (clears bit-5)
▪ Letter address fetch: MOV DL, [BX + DI]
▪ Length fetch: MOV CH, [BX + DI + 5]
Mustafa Shahid · CS-234 COAL Project
7 / 18

## Slide 8
Addressing Modes in Action
BSCS-14B | 500889
Direct
MOV CL, [input_buffer+1]
Named absolute location — reads length field.
Indirect
MOV AL, [SI]
SI points to the current input character.
Indexed
MOV AL, [SI + 2]
Base pointer SI + constant displacement.
Base+Index
MOV DL, [BX + DI]
BX = table base, DI = index × 6.
Base+Idx+Disp
MOV CH, [BX + DI + 5]
Jumps to the length byte of the record.
Logical
AND AL, 0DFh
Bitmask-based lowercase → uppercase.
Mustafa Shahid · CS-234 COAL Project
8 / 18

## Slide 9
Assembly Walk-through
The flow of MAIN at a glance
BSCS-14B | 500889
▪ Initialize DS with the data segment address.
▪ Print banner and prompt via DOS function 09h.
▪ Read user text with buffered input — DOS function 0Ah.
▪ For each character: normalise case with AND AL, 0DFh.
▪ Compute index — digits: SUB + ADD 26; letters: SUB 'A'.
▪ Multiply by RECORD_SIZE (6) to get the table offset.
▪ Loop CH times, emitting each Morse symbol with function 02h.
▪ Invoke PLAY_SOS — audible emergency signal via BEL (07h).
▪ Terminate cleanly with DOS function 4Ch.
Mustafa Shahid · CS-234 COAL Project
9 / 18

## Slide 10
Software Interrupts & the IVT
BSCS-14B | 500889
INT n → consult IVT slot n at 0000:n×4 → run OS handler
INT 21h / 09h
Display $-terminated string
INT 21h / 0Ah
Buffered keyboard input
INT 21h / 02h
Display single character
INT 21h / 4Ch
Terminate with exit code
ASCII 07h
BEL — PC-speaker beep
Mustafa Shahid · CS-234 COAL Project
10 / 18

## Slide 11
Desktop Application
Python + CustomTkinter, fourteen interactive pages
BSCS-14B | 500889
▪ Home dashboard — live session statistics + one-click cards.
▪ Translator: live ASCII ↔ Morse, TXT/WAV export, sample chips.
▪ Live Visualiser: big dot/dash flashes synced to audio.
▪ Emergency SOS: nine indicator lamps + broadcast button.
▪ Telegraph Key: press & hold to tap Morse by hand.
▪ Morse Trainer: decode challenges with score + streak.
▪ Cheat Sheet: click any card to hear that symbol.
▪ CPU Simulator: step, auto-play, speed slider, flag breakdown.
▪ Assembly Viewer, COAL Concepts, ASCII/IVT, 12-q Quiz, Settings.
▪ Starts maximised; responsive from 960×620 to 4K.
Mustafa Shahid · CS-234 COAL Project
11 / 18

## Slide 12
CPU Simulator
Watch the 8086 execute — register by register
BSCS-14B | 500889
What it does
Type any character, click Load. The simulator builds the exact instruction trace the assembly code would execute, ready to step through.
What lights up
AX, BX, CX, DX, SI, DI, SP, BP, IP and FLAGS are shown as hex values. Cyan = modified this step. Amber = IP advance.
Memory view
The full 216-byte Morse lookup table is rendered with an arrow marker that points at base + (index × 6) during each indexed fetch.
Pedagogical win
Students — and examiners — can inspect every step of the translation in natural language, directly inside the demo, without touching emu8086.
Mustafa Shahid · CS-234 COAL Project
12 / 18

## Slide 13
Live Demonstration
BSCS-14B | 500889
Demo script (≈4 minutes):
▪ 1. Double-click Run_Application.bat → window opens maximised.
▪ 2. Home → show statistics strip + click a Translator chip.
▪ 3. Translator → type HELLO WORLD → ▶ Play Audio.
▪ 4. Save .txt and .wav → show the files on disk.
▪ 5. Cheat Sheet → click a few cards → hear each letter.
▪ 6. Telegraph Key → hold SPACE to tap SOS by hand.
▪ 7. Morse Trainer → answer one challenge → show score.
▪ 8. CPU Simulator → type 'S', Load, Play at medium speed.
▪ 9. Live Visualiser → transmit SOS HELP → watch flashes.
▪ 10. Emergency SOS → BROADCAST SOS → lamps sequence.
▪ 11. ASCII/IVT + COAL Concepts + Quiz → walk the cards.
▪ 12. Settings → switch theme → show preferences persist.
Mustafa Shahid · CS-234 COAL Project
13 / 18

## Slide 14
COAL Concepts Demonstrated
BSCS-14B | 500889
Instruction Set Architecture (8086)
Data Definition Directives (DB, EQU)
Direct Addressing Mode
Indirect Addressing Mode
Indexed Addressing Mode
Base + Index + Displacement
Arithmetic & Logical Operations
Software Interrupts (INT 21h)
Interrupt Vector Table
Procedures, CALL / RET, the Stack
I/O Operations (PC Speaker)
Memory Hierarchy via Lookup Tables
Mustafa Shahid · CS-234 COAL Project
14 / 18

## Slide 15
Feature Showcase
What the desktop application delivers
BSCS-14B | 500889
Home
Dashboard with accent-striped feature cards, hero banner and one-click quick actions.
Translator
Live ASCII ↔ Morse, history panel, .txt + .wav export, tone-frequency and unit sliders.
Cheat Sheet
Click any of the 40+ symbol cards to hear the Morse — perfect for memorising during viva prep.
ASCII + IVT
Full ASCII table with Morse codes plus the IVT entries our DOS calls use — printable for study notes.
COAL Quiz
Twelve interactive questions with instant green/red feedback and a final score summary.
Polish
Starts maximised, tooltips on every control, keyboard shortcuts, welcome overlay for new users.
Mustafa Shahid · CS-234 COAL Project
15 / 18

## Slide 16
Opportunities, Challenges & Ethics
BSCS-14B | 500889
Opportunities
Battery-friendly emergency beacons, accessibility tool for speech-impaired users, amateur-radio training.
Challenges
Portability across MASM/TASM/emu8086 dialects; producing clean tones without direct port access.
Ethics
Respect frequency allocations, never transmit false distress calls, always self-identify on air and use the technology to help — never to deceive or eavesdrop.
Mustafa Shahid · CS-234 COAL Project
16 / 18

## Slide 17
Conclusion & Future Work
BSCS-14B | 500889
▪ Three-layer implementation (assembly + simulator + GUI) cleanly maps the entire CS-234 syllabus.
▪ Assembly program demonstrates every major addressing mode.
▪ CPU Simulator makes every instruction observable on screen.
▪ Desktop GUI turns the program into a presentable demo with audio, animation, cheat sheet, ASCII/IVT reference and quiz.
▪ Full documentation — proposal, IEEE report, viva guide.
▪ Future: microcontroller beacon with LED, audio decoder, radio integration, multilingual character support.
Mustafa Shahid · CS-234 COAL Project
17 / 18

## Slide 18
Thank you!
Questions · Feedback · Discussion
Mustafa Shahid | BSCS-14B | CMS 500889
CS-234 Computer Organization & Assembly Language